## Slide 1: Tillamook County Onsite Wastewater Division
Christian Chiola
Environmental Program Manager

## Slide 2: East Tillamook Property Potential residential development

## Slide 3: East Tillamook property soil conditions
Medial loams
Moderately drained
Shallow water table (25-35 inches)
Season high water table possible up to 17 inches

## Slide 4: East Tillamook Property onsite wastewater treatment basics
Local jurisdiction on parcels discharging less than 2500 gallons per day
State review and permitting for systems above 2500 g/day
A 2-bedroom dwelling discharges 300 gallons per day
A 4-bedroom dwelling discharges 450 gallons per day
8 2-bedroom dwellings would discharge 2400 gallons per day

## Slide 5: East Tillamook Property onsite wastewater treatment basics
Primary treatment of sewage is in a septic tank
Advanced treatment reduces the level of contaminants such as BOD (biological oxygen demand, nitrogen and phosphorus
Discharged and dispersed in a drainfield for final treatment

## Slide 6: East Tillamook Property Septic tank and Treatment pod

## Slide 7: East Tillamook Property Drainfield examples

## Slide 8: East Tillamook Property System requirements
Each 8-unit cluster would require up to 4 septic tanks and up to 2 treatment pods each depending on sizing and capacity of units
Each cluster would require up to 800 linear feet of drainfield trenches

## Slide 9: East TillamookProperty Example site plan

## Slide 10: East Tillamook Property Wetlands map

## Slide 11: East Tillamook Property Setbacks
Setbacks from surface waters to septic tanks, treatment units and drainfields is 50 feet
Setbacks to drinking water sources is 100 feet

## Slide 12: Brownfields assessment Grant
FY2025 Brownfields Community-Wide Assessment Cooperative Agreement for $500,000 to provide funding to inventory, assess and conduct clean-up planning for community development projects.

## Slide 13: Brownfields Assessment Grant
100% EPA Funded
Phase I and Phase II Environmental Assessments
Site-Specific clean-up plans
Provide outlets and funding sources for develeopment

## Slide 14: Brownfields assessment Grant
Beaver Elementary School re-development
2 other mixed-use projects in Beaver
Port of Garibaldi processing facilities redevelopment
Beals Alley in Tillamook
Other sites as identified